## Slide 1: GPIO (General Purpose I/O)
Raspberry Pi GPIO

## Slide 2: Raspberry Pi GPIO
GPIO (General Purpose Input/Output)
  General purpose digital I/O interface for embedded system CPU to communicate with peripheral devices
  used to get input from or send output signals to external devices
  program can use each GPIO port as input or output

## Slide 3: Raspberry Pi GPIO
GPIO (General Purpose Input/Output)
  GPIO port: 26 ports in Raspberry Pi
  some port can be used for serial communications (SPI, I2C, UART, etc.)
  power pin: 3.3V, 5V pin
  Raspberry Pi operates 3.3V internally; GPIO pin operates 3.3V as well
  need to use voltage level converter to use 5V device in GPIO pin

## Slide 4: Raspberry Pi Pin Map

## Slide 5: Raspberry Pi Pin Map
GPIO PINs
python
python

## Slide 6: GPIO Control Programming
GPIO control
  control based on file system access using sysfs
    control GPIO port by read/write a special file using sysfs
  control using GPIO control software
    RPi.GPIO: GPIO control module for Python
    WiringPI: GPIO library for C, Python, Ruby

## Slide 7: GPIO Control Programming: LED
LED(Light-emitting diode)

## Slide 8: GPIO Control Programming: LED
LED circuit
V = IR  R = V/I = 3.3/0.02 = 165(Ω)
if R = 220, I = V/R = 3.3/220 = 15(mA)
if R = 1KΩ, I = V/R = 3.3/1000 = 3.3(mA)
3.3V
GND
+
-
bread board

## Slide 9: GPIO Control Programming: LED
Resistor

## Slide 10: GPIO Control Programming: LED
Pi pin connection
  GPIO pin current: 3.3V
  led: 20mA
  resistor: 165Ω ~ 1KΩ
+
-

## Slide 11: GPIO Programming: LED
Python: RPi.GPIO module
  Install:
  Run :
$ sudo apt-get update
$ sudo apt-get install python-dev
$ sudo apt-get install python-rpi.gpio
$ sudo python3
>>> import RPi.GPIO as GPIO
>>> GPIO.setmode(GPIO.BCM)
>>> GPIO.setup(18, GPIO.OUT)
>>> GPIO.output(18, True)
>>> GPIO.output(18, False)
set pin numbering mode

## Slide 12: GPIO Programming: LED
Python: RPi.GPIO module
  methods

## Slide 13: GPIO Programming: LED
Python: Rpi.GPIO module
  Run : blink.py
import RPi.GPIO as GPIO
import time
GPIO.setmode(GPIO.BCM)
GPIO.setup(18, GPIO.OUT)
while (True):
GPIO.output(18, True)
time.sleep(1)
GPIO.output(18, False)
time.sleep(1)
$ sudo python3 blink.py

## Slide 14: GPIO Programming: LED
프로그래밍 실습
  2 leds (red, blue) : gpio 23, 24
  loop: sleep 1 sec for each step
    red, blue: off, off
    red, blue: off, on
    red, blue: on, off
    red, blue: on, on
    위 과정을 계속 반복

## Slide 15: 거리측정센서
Distance sensor
HC-SR04 Ultrasonic sensor
PIR sensor

## Slide 16: Measuring Distance
Ultrasonic sensor (초음파센서)
  Use ultra-sonic echoes : humans can’t hear it
  Provide exact distance readings
Infrared (IR) sensor (적외선센서)
  Passive infrared (PIR) sensors:
    detect the presence of hot things in the measured area by detecting the heat they radiate

## Slide 17: Ultrasonic Sensor
Measuring distance
  uses ultra-sonic echoes
  propagation speed: 340m/s

## Slide 18: Ultrasonic Sensor
HC-SR04 Ultrasonic sensor
  Measurable Range: 2 ~ 400 cm
  Basic principle of work:
    Using IO trigger for at least 10us high level signal
    Module automatically sends eight 40kHz pulses and detect whether there is a pulse signal back
    If the signal back, through high level, time of high output IO duration is the time from sending ultrasonic to returning

## Slide 19: Ultrasonic Sensor
HC-SR04 Ultrasonic sensor
  distance = [(high level time) x velocity of sound (340m/s)] / 2
  distance(cm) = duration(s) * 34000 / 2.
  distance(cm) = [end(μs) – start(μs)] / 29. / 2. ; 29cm/μs
  Electronic Parameters:

## Slide 20: Ultrasonic Sensor
HC-SR04 Ultrasonic sensor
  Timing diagram
5V
5V

## Slide 21: Ranging Project – Source Code
HC-SR04 Ultrasonic sensor
  Trigger, Echo pulse voltage: +5V
  Raspberry Pi: +3.3V
  needs Voltage divider
= 2KΩ
= 3KΩ
Vin= +5V
Vout = Vin * ( )) = 3
R2
R1 + R2
센서 echo pin
RP gpio 핀

## Slide 22: Ranging Project – Source Code
HC-SR04 Ultrasonic sensor: Schematic
  Trig: gpio23
  Echo: gpio24
python
python

## Slide 23: Ranging Program – RPi.GPIO
Program: distance.py
import time
import RPi.GPIO as GPIO
GPIO.setmode(GPIO.BCM)
GPIO_TRIGGER = 23
GPIO_ECHO = 24
print ("Distance measurement starts … \n“)
GPIO.setup(GPIO_TRIGGER, GPIO.OUT)
GPIO.setup(GPIO_ECHO, GPIO.IN)
try:
while True:
start, stop = 0, 0
GPIO.output(GPIO_TRIGGER, False)
time.sleep(2)
GPIO.output(GPIO_TRIGGER, True)
time.sleep(0.00001)
GPIO.output(GPIO_TRIGGER, False)

## Slide 24: Ranging Program – RPi.GPIO
Program: distance.py
while GPIO.input(GPIO_ECHO)==0:
start = time.time()
while GPIO.input(GPIO_ECHO)==1:
stop = time.time()
elapsed = stop-start
distance = (elapsed * 34000.0) / 2.
print ("Distance : %.1f cm\n" % distance)
except KeyboardInterrupt:
print ("Distance measurement ends\n“)
GPIO.cleanup()
GPIO.cleanup()

## Slide 25: PIR Motion Sensor Module
Passive Infrared Sensor: HC-SR501
GND
OUT
Vcc (5~20V)

## Slide 26: PIR Motion Sensor Module
Passive Infrared Sensor: HC-SR501
  Operation

## Slide 27: PIR Motion Sensor Module
Passive Infrared Sensor: HC-SR501
  Single triggering vs. multiple triggering
    Single triggering: if detected, output for a fixed time and disable the detection during a specified time (~3s)
    Retriggering: every time detected, output for a fixed time

## Slide 28: PIR Motion Sensor Module
HC-SR501 Specification
  Voltage: 5V ~ 20V
  Power Consumption: 65mA
  TTL output: 3.3V, 0V
  Trigger mode: L-disable repeat trigger, H-enable repeat trigger (default)
  Sensing range: less than 120 degree, within 7 meters

## Slide 29: Ranging Program – RPi.GPIO
Program: pir_rpi.py
import RPi.GPIO as GPIO
import time
GPIO.setmode(GPIO.BCM)
pirPin = 18
GPIO.setup(pirPin, GPIO.IN)
try:
while True:
if GPIO.input(pirPin) == GPIO.HIGH:
print ("Motion detected!\n“)
else:
print ("No motion\n“)
time.sleep(1)
except KeyboardInterrupt: # ctrl-C
print (“Motion detection ends\n“)
GPIO.cleanup()
GPIO.cleanup()

## Slide 30: Ranging Program – RPi.GPIO
HC-SR501: Schematic
  PIR out: gpio 23
  LED: gpio 25
5V
GND
gpio 23
gpio 25

## Slide 31: Ranging Program – RPi.GPIO
Program: pir_rpi2.py
import RPi.GPIO as GPIO
import time
GPIOIN = 23 # PIR pin
GPIOOUT = 25 # LED pin
GPIO.setmode(GPIO.BCM)
print ("HC-SR501 motion detection start \n“)
GPIO.setup(GPIOIN, GPIO.IN)
GPIO.setup(GPIOOUT, GPIO.OUT)
try:
while True:
state = GPIO.input(GPIOIN)
if(state == True):
print ("state: Motion detected\n“)
else:
print ("state: No Motion\n“)
GPIO.output(GPIOOUT, state)
time.sleep(1)
except KeyboardInterrupt:
print (“Motion detection ends\n“)
GPIO.cleanup()
print ("HC-SR501 motion detection end“)

## Slide 32: 프로그래밍 실습
거리측정센서 Programming
  ultra-sonic sensor: trig 핀을 gpio23, echo 핀을 gpio24 번에 연결
  led: gpio18 번 핀에 연결
    초기상태: OFF
  2초 간격으로 while 반복문 수행:
    초음파센서를 통해 거리 측정
    거리 < 10cm : LED 를 ON
    아니면 : LED 를 OFF
  파이썬 프로그램 작성: distance.py